## Slide 1: Analog & Digital Communications
By KASULA RAGHU
Assistant Professor Dept. of E.C.E. MGIT
9

## Slide 2
9
Subject Code: EC403PC
Google Class Room Code: hglitlo
Google Class Link: meet.google.com/boa-dzzc-oxj

## Slide 3: Course Objectives
9
To develop ability to analyse system requirements of analog and digital communication systems.
To understand the generation, detection of various analog and digital modulation techniques.
To acquire theoretical knowledge of each block in AM, FM transmitters and receivers.
To understand the concepts of baseband transmissions.

## Slide 4: Course Outcomes
9
Upon completing this course, the student will be able to
Analyse and design of various continuous wave and angle modulation and demodulation
techniques
Understand the effect of noise present in continuous wave and angle modulation
techniques.
Attain the knowledge about AM , FM Transmitters and Receivers
Analyse and design the various Pulse Modulation Techniques.
Understand the concepts of Digital Modulation Techniques and Baseband transmission.

## Slide 5: What we will Learn? Analog Communications
9
UNIT – I Amplitude Modulation UNIT – II Angle Modulation UNIT – III Transmitters
UNIT – IV Pulse Modulation (PAM,PWM,PPM) one Line
Digital Communications
UNIT – IV Pulse Code Modulation
UNIT – V Digital Modulation Techniques

## Slide 6: UNIT - I
9
Amplitude Modulation
Need for modulation, Amplitude Modulation - Time and frequency domain description, single tone modulation, power relations in AM waves, Generation of AM waves - Switching modulator, Detection of AM Waves - Envelope detector, DSBSC modulation - time and frequency domain description, Generation of DSBSC Waves - Balanced Modulators, Coherent detection of DSB-SC Modulated waves, COSTAS Loop, SSB modulation - time and frequency domain description, frequency discrimination and Phase discrimination methods for generating SSB, Demodulation of SSB Waves, principle of Vestigial side band modulation.

## Slide 7: Fourier Transforms & Inverse Fourier Transform Formula
9

## Slide 8: Representation
9
F.T. of
x(t) = X(f)
m(t) = M(f)
c(t) = C(f)
s(t) = S(f)
General Notation
Used for Message Signal(KHz) Used for Carrier Signal(MHz) Used for Modulated Signal(MHz)
I.F.T. of
X(f) = x(t)
G(f) = g(t)
M(f) = m(t)

## Slide 9
[ ( f  f )   ( f  f )]
A
2
A cos (2 f t) =
c
c
c
A
2j
A sin (2 f t) =
c
c
c
[ ( f  f )  ( f  f )]
0
- fc
fc
A cos (2 f t) =
m
0
fc
- fc
0
fm
- fm
[ ( f  f )   ( f  f )]
A
2
m
m
A
2
A
2
A
2j
A
2j
A
2
2
9
A
F.T. of Cos & Sin

## Slide 10
2
m( t ) Acos (2 f t) =
c
c
A [ ( f  fc )  M( f  f )]
= A
2j
m( t ) Asin (2 f t)
c
c
c
[ ( f  f )  M( f  f )]
0
c
- fc
f
0
fc
- fc
A
2
A 2j
A
2j
A
2
20/04/2021
KASULA RAGHU
10

## Slide 11: In Time Domain
Message Signal (or) Base Band Signal (or) Modulating Signal (or) Information Signal
23

## Slide 12: In Frequency Domain
23
Band width = ( W - 0) Hz = W Hz

## Slide 13: Introduction
Elements of Communication System:
Communication: It is the process of conveying or information from one point to another.
(Or)
transferring
It is the process of establishing connection or link between two points for information exchange.
23

## Slide 14: Elements of Communication System
23
Information source :
The message or information to be communicated originates in information source. Message can be words, group of words, code, data, symbols, signals etc.
Transmitter :
The objective of the transmitter block is to collect the incoming message signal and modify it in a suitable fashion (if needed), such that, it can be transmitted via the chosen channel to the receiving point.

## Slide 15: Elements of Communication System:
23
Channel :
Channel is the physical medium which connects the transmitter with that of the receiver. The physical medium includes copper wire, coaxial cable, fibre optic cable, wave guide and free space or atmosphere.
Receiver :
The receiver block receives the incoming modified version of the message signal from the channel and processes it to recreate the original (non- electrical) form of the message signal.

## Slide 16: Signal, Message, Information
23
Signal:
It is a physical quantity which varies with respect to time or space or independent or dependent variable.
(Or)
It is electrical waveform which carries information.
Ex: m(t) = Acos(ωt+ϕ)
Where, A= Amplitude or peak amplitude(Volts)
w = Frequency ( rad/sec) ϕ = Phase (rad)

## Slide 17: Types of Signals
Analog or Continuous Signal
Digital Signal
Analog or Continuous Signal: If the
amplitude of signal
continuously varies with respect to time or if the signal contains infinite number of amplitudes, it is called Analog or continuous signal.
23

## Slide 18: Types of Signals Digital Signal: If the signal contains only amplitudes , then it is called digital signal.
23
two discrete
With respect to communication , signals are classified into,
Baseband signal
Bandpass signal
Baseband signal:
If the signal contains zero frequency or near to zero frequency, it is called baseband signal.
Ex: Voice, Audio, Video, Bio-medical signals etc.

## Slide 19: Types of Signals
23
Bandpass signal: If the signal contains band of from base or zero, it is called bandpass signal.
Ex: AM, FM signals.
frequencies far away
Message: It is sequence of symbols. Ex: Happy New Year 2021.
Information: The content in the message is called information. It is inversely proportional to probability of occurrence of the symbol.
Information is measured in bits, decits, nats.

## Slide 20: Limitations of Communication System
23
Technological Problems:
To implement communication systems, Tx, Rx, channel are required
Communication system is expensive and
which requires hardware. complex.
Bandwidth & Noise:
The effect of noise can be reduced by providing
more bandwidth to
stations but due to this less number of stations can only be accommodated.
Signal to Noise Ratio (SNR): Noise should be low to increase channel capacity but it is an unavoidable aspect of communication system.

## Slide 21: Types of Modulation
23

## Slide 22: Modulation : Any Low Frequency/Message Signal m(t) is Multiplied by a High Frequency/Carrier Signal c(t) then the signal get shifted to Right side and Left side to the Frequency of Carrier signal ( i. e M Hz).
23

## Slide 23: c(t) = A cos(2π f t+ϕ) c c
Different Modulations
S.NO | Modulation | What Changed | Constant | Constant
1 | AM | Amplitude | Frequency | Phase
2 | FM | Frequency | Amplitude | Phase
3 | PM | Phase | Amplitude | Frequency
23
*****w. r. t
Amplitude of Message Signal

## Slide 24
23
Modulation
  The process by which some characteristic of a carrier wave is varied in accordance with an information-bearing signal.
  Continuous-wave modulation
    Amplitude modulation
    Frequency modulation
AM modulation family
  Amplitude modulation (AM)
  Double sideband-suppressed carrier (DSB-SC)
  Single sideband (SSB)
  Vestigial sideband (VSB)

## Slide 25: Modulation
23
It is the process of varying the characteristics of high frequency carrier in accordance with instantaneous values of modulating or message or baseband signal.
It is a frequency
(Or)
translation technique which converts
baseband/low frequency signal to band pass/high frequency signal.
Modulation is used at the transmitter. (Filter Used ?)
Demodulation is used at the Receiver. (Filter Used ?)

## Slide 26: Types of Modulation
23
Amplitude Modulation: Amplitude of the carrier is varied in accordance with the instantaneous values of modulating signal.
Frequency Modulation: Frequency of the carrier is varied in accordance with the instantaneous values of modulating signal.
Phase Modulation: Phase of the carrier is varied in accordance with the instantaneous values of modulating signal.

## Slide 27: Need for Modulation
23
To Reduce the height of an antenna
For Multiplexing
For Wideband Signal to Narrow banding
To reduce noise effects
To avoid equipment limitation or to reduce the size of the equipment.

## Slide 28: Amplitude Modulation
The amplitude of the carrier signal varies in accordance with the instantaneous amplitude of the modulating signal.
23

## Slide 29: Carrier & Message Signals
23
The carrier signal is given by,
c(t) = Ac Cos2πfct
Where,
Ac = Maximum amplitude of the carrier signal. fc = Frequency of the carrier signal.
Modulating or baseband signal is given by,
m(t) = Am Cos2πf mt
Where,
Am = Amplitude of the baseband signal.

## Slide 30
23
c(t) = Ac Cos2πfct Carrier Wave
S(t) = [AC + m(t)] Cos2πfct
= Ac [1+ Ka m(t)] Cos2πfct Time Domain Equation of AM
Ka = Amplitude Sensitivity of the Modulator
when m(t) = Zero
then s(t)= c(t) which is called as Unmodulated Carrier
Before Modulation , Magnitude is
After Modulation , Magnitude is
: Ac
: Ac [1+ Ka m(t)]

## Slide 31: Amplitude Modulation
The envelope of s(t) has essentially the same shape as the message signal m(t)
provided that two conditions are satisfied :
  The amplitude of kam(t) is always less than unity
kam(t)  1, for all t
Ka[Maximum Voltage of Message signal ] = Ka[m(t)]max
The carrier frequency fc is much greater than the highest frequency component W of the
message signal
fc  W
Envelope detector
  A device whose output traces KtAhSeULeA nRAvGeHlUope of the AM wave acting as the input signal31
μ = m = μ = m =
20/04/2021

## Slide 32: S(t) = Ac [1+ Ka m(t)] Cos2πfct
S(t) = Ac Cos2πfct + Ac Ka m(t) Cos2πfct
Note: In A.M. Carrier is also Transmitting along with the Modulated signal which is used at the Receiver for Demodulation
The Fourier transform or spectrum of the AM wave s(t)
2
[M ( f  f )  M ( f + f )]
ka Ac
S ( f ) 
2
c c
A c [ ( f  f )   ( f  f )] 
c
c

## Slide 33: S (f)
Ac/2
Ac/2
KaAcM (0)/2
-fc-W -fc
-fc+W
fc fc +W
0 fc-W
Fig : Spectrum of AM signal
f

## Slide 34
BW of AM =34?
20/04/2021
KASULA RAGHU

## Slide 35
For positive
frequencies, the highest frequency
component of the AM wave equals fc+W, and the lowest frequency component equals fc-W. The difference between these two frequencies defines the transmission
is exactly twice
bandwidth BT of the AM wave, which the message bandwidth W
BT  2W

## Slide 36: AM Wave Contains
Carrier Component at fc
LSB from fc-W to fc
USB from fc to fc+W

## Slide 39: Modulation Index
Modulation index or depth of modulation is given by, Vmax - Vmin
Vmax + Vmin
Percentage of modulation index is, Vmax - Vmin
Types of AM with respect to modulation index:
Under Modulation (μ <1)
Critical Modulation (μ =1)
20O/04/v20e21r Modulation (μ >1)
μ =
= Am/Ac
_
_
% μ = Vmax + Vmin
X100
= [Am/Ac ]X100
KASULA RAGHU
39

## Slide 40: Types of AM

## Slide 41: S(t) = Ac [1+ Ka m(t)] Cos2πfct
= Ac [1+ Ka Am Cos2πfm t] Cos2πfct
S(t) = Ac [1+ μ Cos2πfm t] Cos2πfct
Standard Form of A.M.
μ = AmKa = A m/Ac = Modulation Index
Single Tone Modulation of A.M.

## Slide 42: s(t) = Ac Cos2πfct + Ac μ Cos2πfct Cos2πfm t
S(t) = AcCos2πfct + I term
μAc/2Cos[2π(fc+fm)]t + II term
μAc/2Cos[2π (fc-fm)]t III term
I term: Carrier signal with amplitude Ac and frequency fc.
term: Amplitude= μAc/2, frequency= fc+fm , Upper sideband frequency
term: Amplitude= μAc/2, frequency= fc-fm , Lower sideband frequency

## Slide 43: Expanding the equation (2), we get

## Slide 44: f c +fm
Frequency Domain characteristics of single tone AM
f c -fm
S.No | Message | FT | BW of Message | BW of AM Signal
1 | m(t) | M(f) | W | 2W
2 | Cos2πf mt | 0.5 [ ( f  f m )   ( f  f m )] | fm | 2fm

## Slide 46: Power Calculation of AM Wave
AM Wave Contains
Total Power = Carrier Power + USB Power + LSB Power

## Slide 47
Power relations in AM waves:
Consider the expression for single tone/sinusoidal AM wave

## Slide 49
μ = 0
Pt = Pc
μ = 0.5
Pt = 1.125Pc
μ = 1
Pt = 1.5 Pc
Note : When μ is increased from 0 to 1 Power Increased by 50%

## Slide 50: Relationship Between Carrier Power & Side Band Power

## Slide 51: Power Efficiency or Modulation Efficiency
It is the ratio of Utilized Power to the total power in the modulated wave.
μ | = 1 | η = | 33.33%
μ | = 0.75 | η = | 22.22%
μ | = 0.5 | η = | 11.11 %

## Slide 52: Exercise for Multi Tone Modulation
BW= | 2fm2 | if | (fm2 > fm1)
BW= | 2fm1 | if | (fm1 > fm2)

## Slide 53: Multi Tone Modulation
S(t) = Ac [1+ Ka m(t)] Cos2πfct
Where m(t) = Am1 Cos2πfm1 t + Am2 Cos2πfm2 t (for multi-tone) (fm2> fm1 )
= Ac [1+ Ka Am1 Cos2πfm1 t + Ka Am2 Cos2πfm2 t ] Cos2πfct
S(t) = Ac Cos2πfct + Ac μ1 Cos2πfct Cos2πfm1 t + Ac μ2 Cos2πfct Cos2πfm2 t ] where μ = Ka Am ; μ1 = Ka Am1 ; μ2 = Ka Am2

## Slide 57: Generation of AM waves
Square Law Modulator
Switching Modulator
Detection of AM Wave
Envelop Detector

## Slide 58: Generation of AM Wave
Square Law modulator:
Contains 1) non-linear device ,2) Band pass filter, 3) Carrier source and modulating signal

## Slide 61: Switching Modulator

## Slide 62: The total input for the diode at any instant is given by
When the peak amplitude of c(t) is maintained more than that of information signal, the operation is assumed to be dependent on only c(t) irrespective of m(t).
When c(t) is positive, v2=v1 since the diode is forward biased. Similarly,
when c(t) is negative, v2=0 since diode is reverse biased.
Based upon above operation, switching response of the diode is periodic rectangular wave with an amplitude unity and is given by

## Slide 64
The required AM signal is centered at fc can be separated using band pass filter.
The lower cut off-frequency for the band pass filter should be between w and fc-w and the upper cut-off frequency between fc+w and 2fc.
2T0/0h4/2e021filter output is given by the eKAqSUuLAaRAtGiHoUn
64

## Slide 66: Envelope Detector
Note: In AM the Peak Amplitude of the carrier which is also called as the Envelop is varied according to the message signal. So, the envelop of the AM Signal represents the message. E.D is used to track the peak amplitude of the signal
Wave | E.D | 
AM
m (t)
i/p
A co s (2 f c t) 10 sin (2 f c t) e-tcos (2 f c t)
A co s (2 f c t) + B sin (2 f c t)
o/p
A
10
e-t
2 2
√ (A + B )

## Slide 67: Envelope Detector

## Slide 68
The charge time constant (rf + Rs) C must be short compared with the carrier period

## Slide 69: Sketch the Output of the Below Signals when Passed through Envelop Detector

## Slide 71
Advantages
  Generation and demodulation of AM wave are easy
  One Tx & Many Rx
Disadvantages
  More Power taken by Carrier is 66.66%
  BW = 2W Hz of 2fm

## Slide 78: Double Side Band- SC Modulation

## Slide 79: DSB-SC MODULATION
The Advantage of Suppressing the Carrier is Power Saved (66.66%)
Note : We are not Transmitting the Carrier along with Modulated Signal as in AM.

## Slide 81
What about Bandwidth & Power of DSB-SC Wave?
Carrier Power is Saved.
BW Remains Same

## Slide 82: Single Tone Modulation of DSB-SC
S(t) = Ac [1+ Ka m(t)] Cos2πfct
= Ac Cos2πfct + Ac Ka Am Cos2πfct Cos2πfm t
= Ac Ka Am Cos2πfct Cos2πfm t = c(t) m(t)
S(t)
= Ac μ Cos2πfct Cos2πfm t
μ = AmKa = A m/Ac = Modulation Index

## Slide 83: s(t) = Ac μ Cos2πfct Cos2πfm t
S(t) = Acμ/2Cos[2π(fc+fm)]t + Acμ/2Cos[2π (fc-fm)]t I term II term
= Acμ/4 [ ( f  (fc+fm ))   ( f  (fc+fm ))] + Acμ/4 [ ( f  ( fc-fm ))   ( f  ( fc-fm ))]
I term: Amplitude= μAc/2, frequency= fc+fm , Upper sideband frequency II term: Amplitude= μAc/2, frequency= fc-fm , Lower sideband frequency

## Slide 84: Spectrum of Single tone Modulation
S(f)
Ac Am/4
Ac Am/4
Ac Am/4
Ac Am/4
-fc-fm
-fc
-fc+fm
0
fc-fm
fc
fc+fm

## Slide 86: Total Power Required for DSB-SC Wave
S(t) = Ac μ Cos2πfct Cos2πfm t
= Acμ/2Cos[2π(fc+fm)]t + Acμ/2Cos[2π (fc-fm)]t
Total Power = Power in LSB + Power in USB
= (Acμ/2√2) 2 + (Acμ/2√2) 2
= A2 μ2/4
c
= Pcμ2/2
Power Efficiency of Modulation Efficiency = 100%

## Slide 87: Generation of DSBSC Waves
Balanced Modulator (Product Modulator) Ring Modulator
Detection of DSB-SC waves
Coherent Detection or Synchronous Detection or Heterodyne Detection
Costas Receiver

## Slide 88: Balanced Modulator (Product Modulator)

## Slide 89: Ring Modulation

## Slide 91: Thus the ring modulator in its ideal form is a product modulator for square wave carrier and the base band signal m(t). The square wave carrier can be expanded using Fourier series as

## Slide 92
s(t) =
4
𝜋
c
m(t)Cos2πf t -
4
3𝜋
c
m(t)Cos2π(3f )t + ……..
S(f) =
2
𝜋
-
2
3𝜋
[ ( f  3fc )   ( f  3fc )] +……
[ ( f  fc )   ( f  fc )]

## Slide 93: S (f)
2
𝜋
-fc-W
-fc+W
0
fc-W
fc +W
f

## Slide 94: Coherent or Synchronous or Heterodyne Detection

## Slide 96: From the spectrum, it is clear that the unwanted component (first term in the expression) can be removed by the low-pass filter, provided that the cut-off frequency of the filter is greater than W but less than 2fc-
W. The filter output is given by
The quadrature null effect
  The zero demodulated signal, when occurs for Φ=±π/2
  The phase error Φ in the local oscillator causes the detector output to be attenuated
by a factor equal to cos Φ

## Slide 98: Costas Receiver

## Slide 99
Advantages
One to One Communications (Walkie Talkie)
Disadvantages
Less Power than AM
100% Modulation efficiency BW = AM = DSC-SC = 2W Hz

## Slide 100: Single Side Band- SC Modulation

## Slide 102: Single-Sideband Modulation
Single-Sideband Modulation
  Suppress one of the two sideband in the DSB-SC modulated wave
Theory
  A DSB-SC modulator using the sinusoidal modulating wave
m(t)  A cos(2f t)
m m
  The resulting DSB-SC modulated wave is
SDSB (t)  c(t)m(t)
 A A cos(2f t) cos(2f t)
c m c m
Suppressing the second term in the above Eq. the upper and lower SSB modulated wave are
2 2
c m c m c m c m
 1 A A cos[2 ( f  f )t]  1 A A cos[2 ( f  f )t]
(3.14)
2
c m c m
USSB
S (t)  1 A A cos[2 ( f  f )t]
2 2
c m c m c m
USSB c m
S (t)  1 A A cos(2f t) cos(2f t)  1 A A sin(2f t) sin(2f t)
2 2
c m c m c m c m
LSSB
S (t)  1 A A cos(2f t) cos(2f t)  1 A A sin(2f t) sin(2f t)

## Slide 103: S (t)  1 A A cos(2f t) cos(2f t) + 1 A A sin(2f t) sin(2f t)
A sinusoidal SSB modulated wave
2 2
c m c m c m c m
SSB
A
A
c
c
2
c
c
2
SSB
m(t) sin(2f t)

S (t) 
m(t) cos(2
f t) +_
Equation of SSB-SC

## Slide 104: Total Power & Power or Modulation efficiency
Total Power = Power in LSB or
= Power in USB
= (Acμ/2√2)
= Acμ /8
= Pcμ /4
Power Efficiency of Modulation Efficiency = 100%

## Slide 105: Generation of SSB-SC Wave
Frequency Description Method Phase Description Method
Detection of SSB-SC waves
Coherent Detection

## Slide 106: Frequency Description Method

## Slide 107
Upto 500Khz
Upto 20 MHz
Greater Than 20 MHz
Mechanical Filter RC Filter
Crystal filter

## Slide 108: Phase Description Method

## Slide 109: Coherent Detection

## Slide 110
4/20/2021
KASULA RAGHU
110

## Slide 111
2
c c
s(t) = 𝐴𝑐 (m(t) Cos2πf t + m(t)Sin2πf t)
˄
v(t) = [
𝐴𝑐
2
c
(m(t) Cos2πf t + m
c c
(t)Sin2πf t)] Cos(2πf t + φ )
˄
v(t) = [
𝐴𝑐
2
c
(m(t) Cos2πf t + m
c c
(t)Sin2πf t)] Cos(2πf t + φ )
When Passed through LPF
2
vo (t) = 𝐴𝑐 m(t) cos φ +
𝐴𝑐
2
m(t) sin φ
˄
˄
Output of Product Modulator is S(t) x (LO)o

## Slide 112: Time Domain Equation of SSB -SC

## Slide 119
Following the same procedure, we can find the canonical representation for an SS wave
s(t) obtained by transmitting only the lower side band is given by

## Slide 120
Advantages
Voice Communications
Disadvantages
Sharp Cut-off Frequency Filters are not Available Practically
Less Power than AM & DSB-SC 100% Modulation efficiency
BW = WHz or fm Hz

## Slide 121
Vestigial Side Band Modulation
BW= W + fv

## Slide 122: Generation of VSB Modulated Wave

## Slide 123: s(t) = [Ac m(t)Cos2πfc t] h(t)
2
S(f) = 𝐴𝑐 [M( f - fc) + M( f + fc)] H(f)

## Slide 124
4/20/2021

## Slide 125
4/20/2021

## Slide 126
4/20/2021

## Slide 127
20/04/2021
KASULA RAGHU
127

## Slide 128
4/20/2021
KASULA RAGHU
128
Distorted Output

## Slide 130
Perfect Output (Loss is Compensated with the Gain)

## Slide 131: Envelope detection of a VSB Wave plus Carrier

## Slide 132
4/20/2021
KASULA RAGHU
132

## Slide 133: Comparisons of AM,DSBSC,SSB-SC,VSB
S.NO | Parameters | AM | DSB-SC | SSB | VSB
1 | General Equation |  |  |  | 
2 | Singletone Equation |  |  |  | 
3 | General BW |  |  |  | 
4 | Singletone BW |  |  |  | 
5 | Total Power |  |  |  | 
*****Complete the Following

## Slide 134
S.NO | Parameters | AM | DSB-SC | SSB | VSB
6 | Generation Methods |  |  |  | 
7 | Detection Methods |  |  |  | 
8 | Power or Modulation efficiency |  |  |  | 
9 | Applications |  |  |  | 
*****Complete the Following

## Slide 135: Thank You